## Slide 1: In Vehicle Networking Project
Team ProtoCAN
Presented By:
Abishek R – 22MES0011
Ezhil Subbia K – 22MES0006
Kevin Abishek S – 22MES0041
Aadhitya S V – 22MES0007
Ashwin Hariharan R – 22MES0025
Fleet Tracking and Monitoring System

## Slide 2: Features Planned
Uses GPS tracking to monitor the activity of fleet vehicles and assets.
Reliable and scalable data collection for vehicle trackers and embedded sensors.
Advanced and flexible IoT data visualization for both real-time and historical vehicle data.
Customizable end-user dashboards to share data from the vehicle tracking system with end users and customers
Driver driving patterns monitoring – sudden acceleration, deceleration, braking, etc.
Monitoring of critical payload environment – temperature, pressure, humidity, etc

## Slide 3
Dashboard

## Slide 4
Dashboard

## Slide 5: Block Diagram
Tyre pressure sensor
Microcontroller 1 with inbuilt BLE or RF
BLE or RF
GPS
Microcontroller 2
IMU
Temperature Sensor
Humidity Sensor
Barometer
Microcontroller 3
CAN controller 1
CAN controller 2
CAN controller 3
CAN controller 4
Microcontroller 4
IoT Server
GSM/ Wi-Fi/ IoT sim
Web Dashboard
HTTP/MQTT
HTTP

## Slide 6: Connection Establishment
We have built a prototype in which we established CAN Bus communication between two microcontrollers to send temperature and humidity data taken using a sensor. This was done using a CAN controller with an inbuilt CAN transceiver from Microchip.

## Slide 7: Features of CAN Controller Used
Inbuilt High-speed CAN transceiver
8MHZ crystal oscillator
SPI control for expandable Multi CAN bus interface
Supports 1 Mb/s CAN operation
Uses CAN2.0B
120Ω terminal resistance
Low current standby operation
Up to 112 nodes can be connected

## Slide 8: Block diagram with no inbuilt CAN controller
Microcontroller
CAN
Controller
Transmitter Receiver
One-Wire
Sensor
MISO
MOSI
CLK
SS
SPI Master
SPI Slave
CAN Transceiver
CAN TX
CAN bus to TTL
Microcontroller
CAN
Controller
MISO
MOSI
CLK
SS
SPI Master
SPI Slave
CAN Transceiver
CAN RX
CAN bus to TTL
CAN_H Bus
CAN_L Bus
UART
Serial Monitor
RX
TX
(0v-3.3v/0v-5v)
(0v-3.3v/0v-5v)
(0v-3.3v/0v-5v)
(0v-3.3v/0v-5v)
500 Kbits/sec
500 Kbits/sec
Tested Architecture
Xtensa – MIPS (32 bit)
STM – ARM (32 bit)
AVR (8/16 bit)

## Slide 9: CAN Transmitter
The bit rate is set at 500Kbps and clock frequency at 8MHz.
Humidity(h) and Temperature(t) values are obtained from the sensor.
Data length Code(DLC )is set to 8 and we gave the h and t data to the data[0] and data[1] and rest all data with 0 and transmitted over the bus.

## Slide 10: CAN Receiver
The CAN Receiver receives the Temperature and Humidity data from CAN bus.
The CAN receiver is set at 500Kbps and a clock frequency of 8MHz .
The received data is displayed through serial monitor.

## Slide 11: Block diagram with built-in CAN controller
Microcontroller with CAN controller
Transmitter Receiver
One-Wire
Sensor
CAN Transceiver
CAN TX
CAN bus to TTL
Microcontroller with CAN controller
CAN Transceiver
CAN RX
CAN bus to TTL
CAN_H Bus
CAN_L Bus
UART
Serial Monitor
RX
TX
(0v-3.3v/0v-5v)
(0v-3.3v/0v-5v)
Planning to test
Xtensa – MIPS (32 bit)
STM – ARM (32 bit)

## Slide 12: Features of CAN Transceiver
Onboard TJA1050 CAN controller interface chip
5V power supply
High speed (up to 1 Mbaud)
Differential receiver with wide common-mode range for high Electro-Magnetic Immunity (EMI)
An unpowered node does not disturb the bus lines
Input levels compatible with 3.3 V and 5 V devices

## Slide 13
Hardware

## Slide 14: Thank You